## Slide 1
Experimental demonstration of the coexistence of continuous-variable quantum key distribution with an intense DWDM classical channel
Rupesh Kumar
Joint work with
@ TelecomParisTech / CNRS
Hao Qin, Rupesh Kumar, Renaud Gabet, Eleni Diamanti and Romain Alléaume
@ SeQureNet
Paul Jouguet, Sébastien Kunz-Jacques

## Slide 2
Motivations
QKD is a well understood part of quantum information
… but not yet widely adopted
What does QKD need to become a successfull industrial technology ?
ALICE
BOB

## Slide 3
- Performance (Rate, Distance)
Practical Security (Side-channel countermeasures)
Integration in existing infrastructures
Main challenges for QKD development
Chart: 
Fiber Cost | 57.1429 | 72.7273 | 80 | 84.2105 | 86.9565
QKD Cost | 42.8571 | 27.2727 | 20 | 15.7895 | 13.0435
Fiber can be the highest operational cost in QKD network
Example :
QKD Link (75 k$) deployed on a leased dark fiber (2000 $/ km / year)
Cost balance from 1 to 5 years
+ Cost: transversal figure of merit

## Slide 4
Sharing the fiber: Wavelength Division Multiplexing (WDM)
Multiplexing several optical channels in the same fiber
What about QKD in WDM network?
0.2nm – 0.8nm
300 ch
20nm
8-16 ch

## Slide 5
Alice
Bob
Classical
channel
EDFA
Main noise sources in WDM context
Due to finite channel isolation in WDM modules
Spontaneous emission at Lq from EDFA, or
Background emission from classical laser
Inelastic scattering due to
nonlinearity of optical fiber
Other noise sources: Four Wave Mixing and Rayleigh scattering
MUX
DMUX

## Slide 6
Number of photons per ns detection window received by single photon detector (after DEMUX 100 GHz)
Typical amount of noise photons in WDM context
QKD impossible?
With 1 mW launch power
 ~0.3 photons/ns
Consider:
0 dBm (1 mW) classical channel power
100 GHz spacing (DWDM)
-80dB of isolation between channels
Insertion loss -0.5dB
Raman scattering is the main issue

## Slide 7
Cisco DWDM SFP module, Pout = 4 dBm
Previous works on QKD with WDM
Narrow band filters : increases insertion loss.
Demonstration | Year | QKD Wavelength (nm) | Classical Wavelength (nm) | Distance | Ch power
Townsend et al (BT) | 1997 | 1310 | 1550 | 28 | ~ -18dBm
Chapuran et al (Telcordia) | 2009 | 1310 | 1550 | 25 | +2dBm
Lancho et al (Madrid) | 2010 | 1550 | 1310,1490 | 10 | --
Choi et al (Cork) | 2011 | 1310 | 1290,1550 | 10 | 0, -2.7dBm
Eraerds et al (Geneva) | 2010 | 1551.72 | 1555.33, 1555.75 | 50 | -15dBm
Patel et al (Toshiba) | 2012 | 1551.72 | 1555.33,1555.75 | 80 | -18.5dBm
Unconventional classical power: component replacement in classical networks.
Temporal filtering technique : strong constraint on detector jitter (SSPD).
Using classical channels out of the C band: not compatible with DWDM networks.
Is QKD incompatible with modern optical DWDM networks ?
Noise reductions techniques & Drawbacks

## Slide 8
Continuous Variable QKD: promising candidate for DWDM compatibility
Strong advantage of CVQKD: intrinsic filtering of unmatched (noise) photons
Only light coherent with local oscillator (LO) is effectively amplified
108 photons in the LO  80 dB of isolation
Bing Qi, Wen Zhu, Li Qian, Hoi-Kwong Lo, “Feasibility of quantum key distribution through dense wavelength division multiplexing network”, New Journal of Physics 12, 103042 (2010).
Coherent detection (Homodyne detection) acts as a filter.
Balanced Homodyne Detector

## Slide 9
Main source of noise in CVQKD: Raman scattering
Out-band photons (leakage) => unmatched
In-band photons : only matched photons contribute
Raman scattering is the main source of noise for Dist > a few km
Raman anti-stokes forward scattering
Alice
Bob
Classical
channels
Classical
channels
Raman anti-stokes backward scattering
Alice
Bob
Classical
channels
Classical
channels

## Slide 10
Calibrating Raman Scattering Noise on a Balanced Homodyne Detection
LO
Problem : Fluctuation of HD measurement variance with time
Classical
channel
cw
ADM
ADM
MUX
Fiber spool
Solution :
Amplitude modulator to measure shot noise
(improves stability)
AM
(Add Drop Module)
1554.89nm, 1556.56nm, 1557.2nm, 1558.97nm, 1559.79nm
1543.83nm
Two sets to measurements :
Shot noise = N0
Total noise = N0 + NRaman

## Slide 11
Raman scattering calibration measurements: Forward and Backward
hBob= 0.64 bRaman= 3E-9/km.nm ach = 0.2 dB/km
On an homodyne detection, the excess noise at Alice, due to Raman scattering, is maximum around 25 km but is very low:
- 1mw (0dBm) ~ 0.001 N0
- 10mw (10dBm) ~ 0.01 N0

## Slide 12
Full CVQKD + WDM deployment test
- 25 km of fiber
Real-time shot noise estimation
System excess noise ~ 7.10-2
MUX
DMUX
ADM
Fiber Spool
CVQKD
ALICE
CVQKD
BOB
Ch 29
Ch 33
Ch 29
Ch 33
Ch 34
Ch 34
ch34
ch33
ch29

## Slide 13
LO Channel (Ch34)
Classical Channel 33:
Leakage problem
=> Solvable (extra isolation)
Positive key rate (~3 kbit/s)
Successful CVQKD DWDM deployment test at 25 km in
coexistence with an intense (7 dBm) classical channel
Experimental results: excess noise measurement

## Slide 14
Analysis and Prospects
Current noise 0.07 N0
Demonstrated distance limit: > 25 km
- Due to system noise
- Not limited by DWDM channel power
Real shot-noise measurement
(see Poster Paul Jouguet et al.)
- Closes a security loophole (calibration attacks)
Higher losses and stability issues
Improving system stability
(to 0.02 N0 system noise)
=> ~ 50km, 0 dBm should be reachable
No ch
0dBm
7dBm
0.07N0
0.02N0
10
20
30
40
50

## Slide 15
Conclusion and Perspectives
The strong noise filtering, intrinsic to its coherent detection, gives CVQKD a strong advantage in DWDM context
First demonstration of the coexistence, in the C band (DWDM),
of QKD with realistic (several dB) classical channels
Current measurements are compatible with 3 kbit/s at 25 km limited by system noise, not by Raman-induced noise.
Expected limit around 50 km for 0 dBm.

## Slide 16
Thank you